## Slide 1: ECE 340 Lecture 35 MOS Field-Effect Transistor (MOSFET)
The MOSFET is an MOS capacitor with Source/Drain terminals
How does it work?
  Gate voltage (VGS) controls
  mobile charge sheet under
  _______________
  Source-drain voltage (VDS) sweeps
  the mobile charge away, creating ____________ (ID)
Desired characteristics (remember water faucet analogy):
  “On” current __________________
  “Off” current___________________

## Slide 2
First MOSFET patents: Julius Lilienfeld (early 1930s)
This invalidated most of Bardeen,
Brattain and Shockley’s transistor
patent claims in the late 1940s!
But the MOSFET did not work in
practice until the 1960s. Why?

## Slide 3
A modern “n-type” MOSFET (N-MOSFET):
How does it work?
  If VG = 0, any current between source-drain (ID)?
  If VG > 0 what happens (assume source grounded, VS = 0)
  If VGS >> 0 and VDS > 0 what happens?

## Slide 4
Typical 2-D cross-section view of the N-MOSFET:
Note direction of carrier flow,
and of current flow
Gate voltage (VGS) controls
Source-to-Drain current (ID)
“Source” terminal refers to source of _____________
ID
VGS
ID
VGS

## Slide 5
Theory of the MOSFET (*here N-MOSFET):
  When VGS < VT the channel
  is _________________
  When VGS > VT the channel
  is _________________
  If small drain voltage (VDS > 0)
  is applied __________
Will charge sheet move by drift or diffusion?
  Current ≈ width X charge sheet X velocity
What is the inversion charge: |Qinv| ≈
What is the drift velocity: v ≈

## Slide 6
At low VDS, the inversion layer essentially acts like a resistor!
What about higher drain voltages VDS?
Must take into account variation of potential along channel, 0 < Vx < VDS. So inversion layer charge at any point is
|Qinv(x)| = Ci(VGS – VT – Vx)
And the current is:
IDS,lin =
Still linear in VGS voltage! This is the linear region.
When VDS = VGS – VT the channel becomes _____________

## Slide 7
When VDS > VGS - VT the un-inverted (drain depletion) region increases, as does the ____________________
Any increase in VDS:
  Reduces the amount of inversion charge, but…
  Increases the lateral field (charge velocity)
The two effects cancel each other out, so at high VDS the drain current is no longer a function of VDS! The current saturates to a value only dependent on VGS (i.e. charge).
Putting in VDS = VGS – VT (the pinch-off, i.e. saturation condition) in the previous equation:

## Slide 8
Plot and label an example N-MOSFET:
What about IDS vs. VGS?
Z
dox
VT

## Slide 9
Back to the physical picture, why does ID vs. VDS saturate?
Why is this desirable?
  Voltage gain, dVDS/dID because small changes in ID cause large swings in VDS

## Slide 10
What is the “effective mobility” μeff in the MOSFET channel?
Can we look it up in the bulk-silicon charts?
Scattering mechanisms
affecting mobility in channel:
  Charged impurity (Coulomb) scattering
  Lattice vibration (phonon) scattering
  Surface roughness scattering

## Slide 11
Analog applications: Small-Signal MOSFET model
Of all elements in the model… CGS ~ Ci and gm (transconductance dID/dVGS) are essential, the rest are parasitics which must be reduced
Note that a lot of elements are voltage-dependent, e.g. depletion capacitances vary with depletion widths and voltage
ECE 340 Lecture 36 MOSFET Analog Amplifier and Digital Inverter

## Slide 12
Drain current:
Conductance parameters:
See ECE 342, ECE 441
output conductance
transconductance
At low frequency
At high frequency

## Slide 13
Cutoff frequency fmax = frequency where MOSFET no longer amplifies input (gate) signal
Obtained by considering high-freq. small-signal model with output shorted, finding freq. where |iout/iin| = 1
Something we already knew qualitatively  higher MOSFET operating frequency
achieved by decreasing channel
length L, increasing mobility μeff
Smaller = faster for devices
(though parasitics play a big role
in realistic circuits)

## Slide 14
Logic applications: CMOS inverter
Key property: signal regeneration – returns logic outputs (0 or 1=V+=VDD) even in presence of noise
Complementary MOS (CMOS) inverter

## Slide 15
Qualitative operation:
  When Vin = 0  Vout =
  NFET is ________ PFET is __________
  When Vin = VDD  Vout =
  NFET is ________ PFET is __________
Other key property of CMOS inverter: no power consumption while idling in either logic state (only while switching)
Consider PFET as “load” to NFET:
Note “rail-to-rail” logic levels 0 and VDD
Want transition voltage VDD/2, but usually
Lp = Ln which means choose Zp/Zn ≈ 2
because μn ≈ 2μp (for Si)*
*what about other materials?

## Slide 16
A quick look at CMOS power dissipation
Energy consumed while charging capacitive load: EP = _______
CL is discharged through NFET  EN = _________
Total energy dissipated per clock cycle: E = CLVDD2
Frequency f cycles per second  active power P = fCLVDD2
This is very important: fundamental trade-off between speed (f) and power dissipation. Reducing voltage and parasitic C’s is a must to keep power low at higher speeds.

## Slide 17
In reality, there is also passive power (leakage) dissipated by the FETs supposed to be “off”: Poff = IleakVDD
Ioff ~ Ion/1000 in modern technology per transistor
But this can become a headache when you have 100s of millions of “sleeping” transistors (i.e. “passive power” vs. “active power”)!
Ex: see IBM journal of Research & Dev.
http://www.research.ibm.com/journal/rd/504/tocpdf.html